## Slide 1: Verifying Cyber-Physical Systems
Chapter 6 – Specifying Requirements
Abenezer Taye
Apr 19, 2022

## Slide 2: Chapter 6: Specifying Requirements

## Slide 3: Safety Standards
Safety standards: provide guidelines and processes for developing safety-critical systems
DO-178C: a standard given by FAA for determining and certifying the airworthiness of aviation software
  Has five assurance levels for software modules (aka Design Assurance Levels (DALs))
  Modified Condition/Decision Coverage (MC/DC)
  Is a test suite that requires
    Each entry and exit point in the code be invoked
    Each decision take every possible value
    Each condition in a decision take every possible value

## Slide 4: Safety Standards
ISO 26262:
  Has four Automotive Safety Integrity Levels (ASILs) based on exposure to issues that affect the controllability of the vehicle
  Divides probabilities of exposure into five classes
  very low (E1)  high (E4)
  To rate controllability  “controllable” to “difficult to control”
Safety standards are useful for dealing with many potential design and implementation defects.
  However, research shows many areas of autonomous systems are not covered by existing standards
The role of human effort in the task of verification and validation
  Encoding the requirements and models in a verification tool
  Validating the models (checking that the models indeed correspond to the real system)
  Interpreting the output results of the verification tool
  There is no agreed-upon definition for precisely accounting for these human efforts

## Slide 5: Safety requirements
Invariant: capture the idea that “some things always hold” or equivalently, “bad things never happen”.
A candidate invariant I is an invariant if all states along all executions of A satisfy I

## Slide 6: Introduction
Cyber Physical System (CPS): systems that are controlled by computer
Requirements for CPS: the desired or claimed behaviors of the system (aka specifications or properties)

## Slide 7: Testing Vs Verification
Testing: analyzing the resulting behavior data to check whether the requirement is met
For many systems, using testing for establishing system requirements is impossible
  The amount of data required to guarantee a probability of fatality/hr is hrs of data miles (Shalev-Shwartz et al. (2017))
Verification: mathematically proves that a model of the system meets the requirements
System
Initial
condition
Input
Output

## Slide 8: System Design Ecosystem

## Slide 9: Challenges of Verification
Theoretical undecidability :
  There is no algorithm that checks whether a model of CPS meets a requirement.
  To address this  relaxing the verification question (e.g. bounded time horizon or tolerate some false positives)
Practical Scalability :
  Lack of scalability is a huge challenge for the progress in verification
Missing Models :
  Complete models of CPS systems are difficult to come by
    Oftentimes models lack succinct descriptions, are distributed, and are protected intellectual property
Learning-enabled systems and missing requirements :
  Recent CPS systems use DNN  lack models and requirements

## Slide 10: Chapter 2: MODELING COMPUTATION

## Slide 11: Introduction
Aim: how can we develop a mathematical model for computation
We use differential equations to model physical systems  how about computation?
Automaton: 19th century word used to describe mechanical dolls
In mathematics, we use automaton to describe the rules of state change of any computational process
  Aka, discrete-time transition system or a state machine

## Slide 12: Example: JK Flip-Flop
clk | J | k | Q
0 | 0 | 0 | previous
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | toggle
Parts of specification
Actions: lists various types of rules for state change
Variables: lists the state variables
Transitions: lists the state change rules for each of the actions

## Slide 13: Specifying automata
State variables:
  A state represents the information necessary for predicting the future of an automaton
Valuation:
  Maps each state variable name to a value
Predicates:
  A Boolean–valued formula involving the variables in V (we use it as a requirement)
    For example: the state satisfies the formula
    Because
Transitions:
  Specify the rules for state change in a computation

## Slide 14: Automata
An automaton is a tuple , where
V is a set of state variables and val(V) is valuations of V
is a set of start states
A is a set of actions
is called the set of transitions

## Slide 15: Semantics
Execution : an alternating, possibly infinite, sequence of states and actions
  Each is a state val(V)
  Each is an action in A
  Each consecutive triple is a valid transition in
Reachable state : a state is reachable if there exists a finite execution that ends at v
Invariant: a set of states that contains all of ’s reachable states

## Slide 16: Thank You!!!